SPECIFICATIONS

| System Configuration | CPU | Rockchip RK3229 Quad-Core Cortex-A7 |
| --- | --- | --- |
|  | GPU | Penta-Core ARM Mali-400MP2 |
|  | FLASH | 16GB NAND FLASH |
|  | SDRAM | 2GB DDR3 |
| Main Features | OS | Android 8.1 |
|  | KD | 18 |
|  | WIFI | 2.4GHz |
|  | 3D | Hardward 3D graphics acceleration |
|  | Decoder format | HD MPEG1/2/4,H.264, HD AVC/VC-1, RM/RMVB ,Xvid/DivX3/4/5/6 , RealVideo8/9/10,VP9 |
|  | Media format | Avi/Rm/Rmvb/Ts/Vob/Mkv/Mov/ISO/wmv/asf/flv/dat/mpg/mpeg |
|  | Music format | MP3/WMA/AAC/WAV/OGG/AC3/DDP/TrueHD/DTS/DTS/HD/FLAC/APE |
|  | Photo format | HD JPEG/BMP/GIF/PNG/TIFF |
|  | USB host | 2 High speed USB 2.0,support U DISK and USB HDD |
|  | Card reader | SD/SDHC/MMC cards |
|  | HDD file system | FAT16/FAT32/NTFS |
|  | Support Subtitle | SRT/SMI/SUB/SSA/IDX+USB |
|  | HD video output | SD/HD max.1920x1080 pixel |
|  | OSD languages | English/French/German/Spanish/Italian/ etc multilateral languages |
|  | LAN | Ethernet: 10/100M, standard RJ-45 |
|  | Wireless | Built in 2.4G WiFi |
|  | Mouse/ Keyboard | Support mouse and keyboard via USB; Support 2.4GHz wireless mouse and keyboard via 2.4GHz USB dongle |
|  | HD | HD 2.0 up to 4k2k Output |
|  | 4K2k HD Decoding | 4k2k H.265 Hardware Video Decode and 4k2k Output |
|  | 1080P/AV/Dolby/3G | Support |
|  | SPDIF/IEC958 | Coaxial |
| Software Specifications | Network Function | Skype chatting, Picasa, Youtube, Flicker, Facebook, Online movies, etc |
|  | Other feature | Free Internet searching,thousands of android applications,many kinds of games,etc. |
| Power Supply | Power Supply | DC 5V/2A |
|  | Power Indicator (LED) | Power ON: Blue |